## Slide 1: Multimedia System and Virtual Environment
CSE – 310
Lecture 7
MIDI
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 2
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Components of a MIDI System
MIDI terminology
MIDI Concepts
MIDI Message
MIDI Advantages
MIDI Disadvantages
Outline

## Slide 3
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
MIDI (Musical Instrument Digital Interface)
Definition of MIDI: a protocol that enables computer, synthesizers, keyboards, and other musical device to communicate with each other
Components of a MIDI System:
  Synthesizer (a sound generator)
  Sequencer (a music editor)
  Track (to organize the recordings)
  Channel (to separate information in a MIDI system)
  Timbre (the quality of the sound)
  Pitch (musical note that the instrument plays)
  Voice (the portion of the synthesizer that produces sound)
  Patch (the control settings that define a particular timbre)

## Slide 4
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Synthesizer: An electronic instrument, often played with a keyboard, that combines simple waveforms to produce more complex sounds.
Sequencer: A music sequencer is a device designed to play back musical notation.
Track: Sound track of background music played under the action in a film or videotape.
Channel: A discrete portion of the complete MIDI signal that can include as many as 16 channels. Each channel carries independent messages; individual instruments tune into these, just as a television tunes in to one of many channels.
MIDI terminology

## Slide 5
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Timbre: The tonal color of a sound, which reflects its harmonic content and envelope.
Patch: A specific sound on a keyboard. The term originated with early synthesizers, which required hooking various components together with “patch” cords to create a sound.
Pitch: Pitch is a perception of sound by human beings. It measures how ‘high’ is the sound as it is perceived by a listener.
Sound: The sound made by the vibration of vocal folds modified by the resonance of the vocal track.
MIDI terminology

## Slide 6
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
a) MIDI is a scripting language — it codes "events" that stand for the production of sounds. e.g., a MIDI event might include values
for the pitch of a single note, its duration, and its volume.
b) MIDI is a standard adopted by the electronic music industry for controlling devices, such as synthesizers and sound cards, that produce music.
c) The MIDI standard is supported by most synthesizers, so sounds created on one synthesizer can be played and manipulated on another synthesizer and sound reasonably close.
d) Computers must have a special MIDI interface, but this is incorporated into most sound cards. The sound card must also have both D/A and A/D converters.
MIDI Overview

## Slide 7
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
General MIDI: A standard mapping specifying what instruments will be associated with what channels.
a) In General MIDI, channel 10 is reserved for percussion instruments, and there are 128 patches associated with standard instruments.
b) For most instruments, a typical message might be a Note On message (meaning, e.g., a keypress and release), consisting of what channel, what pitch, and what "velocity" (i.e., volume).
c) For percussion instruments, however, the pitch data means which kind of drum.
d) A Note On message consists of "status" byte — which channel, what pitch — followed by two data bytes. It is followed by a Note Off message, which also has a pitch (which note to turn off) and a velocity (often set to zero).
MIDI Concepts

## Slide 8
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 9
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 10
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Channel messages: can have up to 3 bytes:
The first byte is the status byte (the opcode, as it were); has its most significant bit set to 1.
The 4 low-order bits identify which channel this message belongs to (for 16 possible channels).
The 3 remaining bits hold the message. For a data byte, the most significant bit is set to 0.
Voice messages:
This type of channel message controls a voice, i.e., sends information specifying which note to play or to turn off, and encodes key pressure.
Voice messages are also used to specify controller effects such as sustain, vibrato, tremolo, and the pitch wheel.
Channel messages

## Slide 11
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Channel mode messages:
Channel mode messages: special case of the Control Change message → opcode B (the message is &HBn, or 1011nnnn).
However, a Channel Mode message has its first data byte in 121 through 127 (&H79–7F).
Channel mode messages determine how an instrument processes MIDI voice messages: respond to all messages, respond just to the correct channel, don't respond at all, or go over to local control of the instrument.
Channel messages

## Slide 12
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
System Messages:
System messages have no channel number — commands that are not channel specific, such as timing signals for synchronization, positioning information in pre-recorded MIDI sequences, and detailed setup information for the destination device.
Opcodes for all system messages start with & HF.
System messages are divided into three classifications, according to their use:
      1. System common messages
      2. System real-time messages
      3. System exclusive message
Channel messages

## Slide 13
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
System common messages: relate to timing or positioning.
System real-time messages: related to synchronization.
System exclusive message: included so that the MIDI standard can be extended by manufacturers.
a) After the initial code, a stream of any specific messages can be inserted that apply to their own product.
b) A System Exclusive message is supposed to be terminated by a terminator byte &HF7.
c) The terminator is optional and the data stream may simply be ended by sending the status byte of the next message.
Channel messages

## Slide 14
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
MIDI files are much more compact than digital audio files, and the size of a MIDI file is completely independent of playback quality. In general, MIDI files will be 200 to 1,000 times smaller than digital audio files.
MIDI files don’t take much RAM, disk space, and CPU resources.
MIDI files embedded in web page and play more quickly than their digital equivalents.
MIDI files sound better than digital audio files.
You can change the length of a MIDI file without changing the pitch of the music or degrading the audio quality.
MIDI data is completely editable right down to the level of an individual note.
You can manipulate the smallest detail of a MIDI composition in ways that are impossible with digital audio.
MIDI Advantages

## Slide 15
MIDI
Lecture 7
Dept. of Computer Science and Engineering, University of Rajshahi
Playback will be accurate only if the MIDI playback device is identical to the device used for production.
MIDI cannot easily be used to play back spoken dialog.
MIDI Disadvantages