## Slide 1: Multimedia System and Virtual Environment
CSE – 310
Multimedia Networks
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 2
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Internet protocol
Transmission Control Protocol
User Datagram Protocol
WAN Switch Functionality
Asynchronous Transfer Mode
Outline

## Slide 3
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Internet protocol
Application: supporting network applications
  FTP, SMTP
Transport: host-host data transfer
  TCP, UDP
Network: routing of datagrams from source to destination
  IP, routing protocols
Link: data transfer between neighboring network elements
  PPP, Ethernet
Physical: bits “on the wire”
application
transport
network
link
physical
TCP/IP

## Slide 4
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
The Transport Layer
Concerned with end-to-end data transfer between end systems (hosts)
Transmission unit is called segment
TCP/IP networks such as the Internet provides two types of services to applications
  “connection-oriented” service – Transmission Control Protocol (TCP)
  “connectionless” service - User Datagram Protocol (UDP)

## Slide 5
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
(TCP) Transmission Control Protocol
TCP is an alternative transport layer protocol supported by IP.
TCP provides:
    Connection-oriented
    Reliable
    Full-duplex
    Byte-Stream

## Slide 6
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Connection-Oriented
Connection oriented means that a virtual connection is established before any user data is transferred.
If the connection cannot be established - the user program is notified.
If the connection is ever interrupted - the user program(s) is notified.
Reliable
Reliable means that every transmission of data is acknowledged by the receiver.
If the sender does not receive acknowledgement within a specified amount of time, the sender retransmits the data.
(TCP) Transmission Control Protocol

## Slide 7
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
(TCP) Transmission Control Protocol
Byte Stream
The connection is treated as a stream of bytes.
The user application does not need to package data in individual datagrams.
Buffering
TCP is responsible for buffering data and determining when it is time to send a datagram.
It is possible for an application to tell TCP to send the data it has buffered without waiting for a buffer to fill up.
Full Duplex
TCP provides transfer in both directions.

## Slide 8
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
UDP is a transport protocol communication between processes
  No handshaking
  Connectionless Service
  Send whenever and however you want
  A “best effort” service
    No reliability
    No congestion & flow control services
(UDP) User Datagram Protocol

## Slide 9
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
The Network Layer
End systems inject datagrams in the networks
A transmission path is determined for each packet (routing)
A “best effort” service
  Datagrams might be lost
  Datagrams might be arrive out of order
  Jitter in arrival of datagrams from the same stream
Analogy: Postal system

## Slide 10
WAN Switch Functionality
WAN switches use store and forward technology.
The store operation occurs when the packet arrives: the I/O hardware copies the packet, sticks it in memory, and signals the processor to forward the packet.
The forward operation is the act of removing the packet from memory, and sends it to the appropriate interface.
Storing the packets also leads to a form of queuing for each interface.
If the destination interface is busy, the packet is queued until the destination interface is idle, then the forward occurs.
Dept. of Computer Science and Engineering, University of Rajshahi
Multimedia Networks
Lecture 14

## Slide 11
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
The store and forward paradigm allows to handle the maximum bandwidth of the WAN connection.
A hierarchical scheme is used with WAN addressing.
The simplest form of this scheme: The first part of the address holds the destination switch, the second part holds the specific machine that the packet is destined for on that switch.
WAN Switch Functionality

## Slide 12
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Circuit Switching
There are three phases in circuit switching:
  Establish
  Transfer
  Disconnect
In modern circuit-switched networks, electronic signals pass through several switches before a connection is established.
No other network traffic can use those switches.
The resources remain dedicated to the circuit during the entire data transfer and the entire message follows the same path.

## Slide 13
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Circuit Switching
With the expanded use of the Internet for voice and video, analysts predict a gradual shift away from circuit-switched networks.
A circuit-switched network is excellent for data that needs a constant link from end-to-end. For example real-time video.
  Advantages:
      Circuit is dedicated – no interference, no sharing
      Guaranteed the full bandwidth for the duration of the call
      Guaranteed Quality of Service

## Slide 14
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Circuit Switching
Disadvantages:
    Inefficient – the equipment may be unused, if no data is being sent, the dedicated line still remains open
    Takes a relatively long time to set up the circuit
    During a crisis or disaster, the network may become unstable or unavailable.
    It was primarily developed for voice traffic rather than data traffic.

## Slide 15
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Packet Switching
Data transmitted in small packets
  Typically 1000 bytes
  Longer messages split into series of packets
  Each packet contains a portion of user data plus some control info (such as addressing info or packet type)
Packets are received, stored briefly (buffered) and passed on to the next node
  Store and forward (only ATM does not do this)

## Slide 16
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Packet Switching
Advantages
  Line efficiency
    Single node to node link can be shared by many packets over time
    Packets queued and transmitted as fast as possible
  Data rate conversion
    Each station connects to the local node at its own speed
    Nodes buffer data if required to equalize rates
  Packets are accepted even when network is busy
    Delivery may slow down
  Priorities can be used
Disadvantages
  Ineffective when the network is congested and becomes unreliable by severely delaying or losing packets

## Slide 17
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Frame Relay
Data is divided into small, variable sized cells, up to 16,000 octets.
Up to 1.544Mbps transmission rate.
Shared bandwidth with other connections.
Reduction of error checking: no more acknowledgment, no more error control.
Reduction of layers: The multiplexing and switching virtual circuits are changed from layer 3 in X.25 to layer 2. Layer 3 of X.25 is eliminated.

## Slide 18
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
Cell Relay (ATM)
ATM standard is widely accepted by common carriers as mode of operation for communication.
ATM is a form of cell switching using small fixed-sized packets.

## Slide 19
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
ATM Conceptual Model Four Assumptions
ATM network will be organized as a hierarchy.
    User’s equipment connects to networks via a UNI (User-Network Interface).
    Connections between provided networks are made through NNI (Network-Network Interface).
ATM will be connection-oriented.
Vast majority of ATM networks will run on optical fiber networks with extremely low error rates.
ATM must support low cost attachments.

## Slide 20
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
ATM Connections
two levels of ATM connections:
virtual path connections
virtual channel connections
indicated by two fields in the cell header:
  virtual path identifier VPI
  virtual channel identifier VCI
Physical Link
Virtual Paths
Virtual Channels

## Slide 21
ATM Cell Format
GFC= General Flow Control VPI=Virtual Path Identifier
VCI=Virtual Channel Identifier PT=Payload Type
CLP=Cell Loss Priority HEC=Header Error Check
Header
Payload
5 Bytes
48 Bytes
Basic ATM Cell Format
Dept. of Computer Science and Engineering, University of Rajshahi
Multimedia Networks
Lecture 14
GFC(4b)
VPI(8b)
VCI(16b)
PT
(3b)
CLF
(1b)
HEC
(8b)

## Slide 22
Multimedia Networks
Lecture 14
Dept. of Computer Science and Engineering, University of Rajshahi
ATM Layers and Sublayers
AAL
CS
SAR
ATM
Physical
TC
PMD
Transport
Physical
Data Link
Network
OSI
ATM
AAL= ATM Adaptation Layer
CS = Convergence Sublayer
SAR = Segmentation and Reassembly
TC = Transmission Convergence
PMD = Physical Medium Dependent