## Slide 1: Multimedia System and Virtual Environment
CSE – 310
Multimedia Networks
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 2
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
Outline
RTP (Real Time Transport Protocol)
RSVP (Resource ReSerVation Protocol)
RTCP (Resource Time Control Protocol)
RTSP (Real Time Streaming Protocol)

## Slide 3
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
Real-Time Protocol (RTP)
RTP specifies packet structure for packets carrying audio, video data
RTP packet provides
  payload type identification
  packet sequence numbering
  time stamping
RTP runs in end systems
RTP packets encapsulated in UDP segments
interoperability: if two Internet phone applications run RTP, then they may be able to work together

## Slide 4
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTP runs on top of UDP
RTP libraries provide transport-layer interface that extends UDP

## Slide 5
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTP Example
consider sending 64 kbps PCM-encoded voice over RTP.
application collects encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk.
audio chunk + RTP header form RTP packet, which is encapsulated in UDP segment
RTP header indicates type of audio encoding in each packet
RTP header also contains sequence numbers, timestamps.

## Slide 6
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTP and QoS
RTP does not provide any mechanism to ensure timely data delivery or other QoS guarantees.
RTP encapsulation is only seen at end systems (not) by intermediate routers.
  routers providing best-effort service, making no special effort to ensure that RTP packets arrive at destination in timely matter.

## Slide 7
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTP Header
Payload Type (7 bits): Indicates type of encoding currently being used.
Sequence Number (16 bits): Increments by one for each RTP packet sent, and used to detect packet loss and to restore packet sequence.
Timestamp (32 bytes long): The timestamp records the first octet of the packet is sampled; it is set by the sender.
Synchronization Source (SSRC 32 bits long): Identifies source of RTP stream. Each stream in RTP session should have distinct SSRC.
Contributing Source (CSRC 32 bits long): Identifies source of contributors.

## Slide 8
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
Real-Time Control Protocol (RTCP)
works in conjunction with RTP.
each participant in RTP session periodically transmits RTCP control packets to all other participants.
each RTCP packet contains sender and/or receiver reports
  report statistics useful to application: # packets sent, # packets lost, interarrival jitter, etc.
feedback can be used to control performance
  sender may modify its transmissions based on feedback

## Slide 9
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTCP - Continued
each RTP session: typically a single multicast address; all RTP /RTCP packets belonging to session use multicast address.
RTP, RTCP packets distinguished from each other via distinct port numbers.
to limit traffic, each participant reduces RTCP traffic as number of conference participants increases

## Slide 10
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTCP Packets
Receiver report packets:
fraction of packets lost, last sequence number, average interarrival jitter
Sender report packets:
SSRC of RTP stream, current time, number of packets sent, number of bytes sent
Source description packets:
e-mail address of sender, sender's name, SSRC of associated RTP stream
provide mapping between the SSRC and the user/host name

## Slide 11
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTSP (Real Time Streaming Protocol)
RTSP:
client-server application layer protocol
user control: rewind, fast forward, pause, resume, repositioning, etc…
RTSP messages sent out-of-band:
RTSP control messages use different port numbers than media stream: out-of-band.
media stream is considered “in-band”.

## Slide 12
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RTSP Operation

## Slide 13
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RSVP: Resource Reservation Protocol
  “ … allow users to communicate requirements to network in robust and efficient way.”
Figure 16.4: A scenario of network resource reservation with RSVP
RSVP (Resource Reservation Protocol)

## Slide 14
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RSVP Design Goals
accommodate heterogeneous receivers (different bandwidth along paths)
accommodate different applications with different resource requirements
make multicast a first class service, with adaptation to multicast group membership
control existing multicast/unicast routing, with adaptation to changes in underlying unicast, multicast routes
control protocol overhead to grow (at worst) linear in # receivers
modular design for heterogeneous underlying technologies

## Slide 15
Multimedia Networks
Lecture 16
Dept. of Computer Science and Engineering, University of Rajshahi
RSVP: overview of operation
senders, receiver join a multicast group
    done outside of RSVP
    senders need not join group
sender-to-network signaling
    path message: make sender presence known to routers
    path teardown: delete sender’s path state from routers
receiver-to-network signaling
    reservation message: reserve resources from sender(s) to receiver
    reservation teardown: remove receiver reservations
network-to-end-system signaling
    path error
    reservation error