## Slide 1: Multimedia System and Virtual Environment
CSE – 310
Lecture 8
VIDEO
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 2: Outline
Basic Video Properties
Signal Format
Analog and Digital Video
Chroma Subsampling
Interlaced/Progressive Scanning
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 3: Basic Video Properties
Representation of Video Signals
  Visual Representation
    To present the observer with as realistic as possible a representation of a scene
  Transmission of Video Signals
    Television Systems
  Video Digitization
    Digital Television
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 4: Visual Representation
In order to accurately convey both spatial and temporal aspects of a scene, the following properties are considered
  Vertical Details and Viewing Distance
    The geometry of a television image is based on the ratio of the picture width W to the picture height H (W/H), called the aspect ratio.
      Conventional aspect ratio is 4:3.
    The angular field of view is determined by the viewing distance, D, and is calculated as D/H.
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 5: Visual Representation
Horizontal Detail and Picture Width
  Can be determined from the aspect ratio
Total detail content of a picture
  Since not all lines (horizontal and vertical) are visible to the observer, additional information can be transmitted through them.
Depth perception
  Depth is a result of composing a picture by each eye (from different angles)
  In a flat TV picture
    Perspective appearance of the subject matter
    Choice of focal length of the camera lens and changes in depth focus
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 6: Visual Representation
Luminance
  RGB can be converted to a luminance (brightness signal) and two color difference signals (chrominance) for TV signal transmission
Temporal Aspects of Illumination
  A discrete sequence of still images can be perceived as a continuous sequence.
    The impression of motion is generated by a rapid succession of barely differing still pictures (frames).
      Rate must be high enough to ensure smooth transition.
      Rate must be high enough so that the continuity of perception is not disrupted by the dark intervals between pictures
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 7: Visual Representation
Continuity of Motion
  Continuity is perceived with at least 15 frames per second.
    To make motion appear smooth in a recorded film, a rate of 30 frames per second is needed.
      Films recorded with 24 frames per second look strange when large objects close to the viewer move quickly.
    NTSC (National Television Systems Committee) Standard
      Original: 30 frames/second
      Currently: 29.97 frames/second
    PAL (Phase Alternating Line) Standard
      25 frames per second
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 8: Visual Representation
Flicker
  If the refresh rate is low, a periodic fluctuation of the perceived brightness can result.
    Minimum to avoid flicker is 50 Hz.
    Technical measures in movies and TV have allowed lower refresh rates.
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 9: Chrominance
Chrominance (chroma ) is the signal used in video systems to convey the color information of the picture, separately from the accompanying luma signal (or Y).
  Chrominance is usually represented as two color-difference components: U = B − Y (blue − luma) and V = R − Y (red − luma).
  Each of these difference components may have scale factors and offsets applied to it, as specified by the applicable video standard.
  In composite video signals, the U and V signals modulate a color subcarrier signal, and the result is referred to as the chrominance signal.
  The phase and amplitude of this modulated chrominance signal correspond approximately to the hue and saturation of the color.
  In digital-video and still-image color spaces such as YCbCr, the luma and chrominance components are digital sample values.
Luma represents the brightness in an image (the "black and white“ portion of the image).
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 10: Signal Formats
Computer Video Formats
  Color Graphics Adapter (CGA)
    Resolution: 320 x 200
    2 bits / pixel
  Enhanced Graphics Adapter (EGA)
    Resolution: 640 x 350
    4 bits / pixel
  Video Graphics Array (VGA)
    Resolution: 640 x 480
    8 bits / pixel
  Super Video Graphics Array (SVGA)
    Resolution: 1024 x 768, 1280 x 1024, 1600 x 1280
    8 bits / pixel
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 11: Types of Video Signals
Dept. of Computer Science and Engineering, University of Rajshahi
Component video
  Three separate signals for tristimulus color representation or luminance-chrominance representation
  Pro: higher quality, no cross talk
  Con: need high bandwidth and synchronization
Composite video
  Multiplex into a signal
  Historical reason for transmitting color TV through monochrome channel
  Pro: save bandwidth
  Con: cross talk
S-video: luminance sig. + single multiplexed chrominance sig.
  Pro: less color detail
  Con: cross talk

## Slide 12
Dept. of Computer Science and Engineering, University of Rajshahi
Color Coding: RGB
An RGB signal consists of separate signals for red, green, and blue.
Every color can be encoded as a combination of these three primary colors using additive color mixing.
The value of R, G, and B are normalized such that white results when R + G + B = 1 in the normalized representation.

## Slide 13: Color Coding: YUV
  Y is luminance
  UV are chrominance
YUV from RGB
  Y =.299R+.587G+.114B U = 0.492 * (B - Y) V = 0.877 * (R - Y)
Y
U
V
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 14: YCrCb
Subset of YUV that scales and shifts the chrominance values into range 0..1
  Y = 0.299R + 0.587G + 0.114B Cr = ((B-Y)/2) + 0.5 Cb = ((R-Y)/1.6) + 0.5
Dept. of Computer Science and Engineering, University of Rajshahi
Y
Cr
Cb

## Slide 15: YIQ
YIQ from RGB
  Y = 0.299R + 0.587G + 0.114B I = 0.60R - 0.28G – 0.32B Q = 0.21R - 0.52G + 0.31B
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 16: Analog Video
NTSC Video (National Television Standards Comittee)
    Originated in the US
    Uses color carriers of approx. 4.429 MHz or approx. 3.57 MHz.
    With suppressed color carrier, it uses quadrature amplitude modulation
    Refresh rate: 30Hz
    # horizontal lines: 525
    Aspect ratio 4:3
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 17: Analog Video
  SECAM Video (System Electronic Couleur Avec Memoire)
    France and Eastern Europe
    With suppressed color carrier, it uses frequency modulation
    Refresh rate: 25Hz
    # horizontal lines: 625
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 18: Analog Video
  PAL Video (Phase Alternating Line)
    Parts of Western Europe
    Uses color carriers of approx. 4.43 MHz
    With suppressed color carrier, it uses quadrature amplitude modulation
    Refresh rate: 25Hz
    # horizontal lines: 525
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 19: Digital Video
Advantages:
    Storing video on digital devices ready to be processed (noise removal, cut and paste, and so on) and integrated into various multimedia applications.
    Direct access which makes nonlinear video editing simple
    Repeated recording without degradation of image quality
    Ease of encryption and better tolerance to channel noise
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 20: High-Definition TV (HDTV)
  Research began in Japan, 1968
  Third Technological Shift (after black and white and color TV)
  The goal was to “integrate” the viewer with the events happening on the screen
  Resolution
    More than 1000 scanning lines
      Approximately double the resolution of conventional TV
    Higher video bandwidth
      About five times that of conventional TV
    Resolutions Recommended
      High 1440 Level: 1440 x 1152
      High Level: 1920 x 1152
      Later, 2k x 2k pixels
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 21: High-Definition TV (HDTV)
  Frame Rate
    No agreement on a fixed frame rate worldwide
    50 or 60 frames per second
  Aspect Ratio
    Originally 16:9
    Currently 4:3
  Interlaced and/or progressive scanning formats
    Conventional systems supported interlaced scanning formats
    HDTV supports both.
  Viewing Conditions
    Screen area should be bigger than 8000cm2 for “real” scenes
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 22: Interlaced Scanning
Developed for Cathode Ray Tube (CRT)-based TV monitor displays
Made up of 576 visible horizontal lines across a standard TV screen.
Interlacing divides these into odd and even lines and then alternately refreshes them at 30 frames per second.
The slight delay between odd and even line refreshes creates some distortion or 'jaggedness'. This is because only half the lines keeps up with the moving image while the other half waits to be refreshed.
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 23: Progressive Scanning
Progressive scanning scans the entire picture line by line every sixteenth of a second.
Computer monitors do not need interlace to show the picture on the screen, so there is virtually no "flickering" effect.
Dept. of Computer Science and Engineering, University of Rajshahi

## Slide 24: Chroma Subsampling
Dept. of Computer Science and Engineering, University of Rajshahi
Since human see color with much less spatial resolution than black and white, it makes sense to decimate the chrominance signal.
Here label numbers are given stating how many pixel values, per four original pixels, are actually sent.
Chroma subsampling scheme “4:4:4” indicates that no chroma subsampling is used.

## Slide 25: Chroma Subsampling
Dept. of Computer Science and Engineering, University of Rajshahi